## Slide 1
Brainstorm源分析
Source
Model
EEG
Channel
Position
Head Model
记录于头皮
的脑电数据
描述头部几何形状和组织电导率, 也叫Forward Model. 这里使用OpenMEEG BEM计算头模型.
Dipole fitting method: 一个偶极子表示局部神经核团的突触后端的电活动, 既有大小又有方向。
Distributed models: 大量位置固定的偶极子 ,有大小无方向。
ERP

## Slide 2
Brainstorm源分析
解剖和空间信息
Head
Model
Source
Model
Channel
Position
功能数据(MEG/EEG)
Processing of
functional data
Inverse solution
visualization
Single sphere
Overlapping spheres
OpenMEEG BEM
Forward solution
Averaging & Noise covariance estimation
计算方法：
1.Current density map
2.dSPM---Implements dynamical Statistical Parametric Mapping
3.sLORETA---Standardized Low Resolution brain Electromagnetic TomogrAphy
源模型偶极子的指向：
1.Contrained: Normal to cortex--- Only for "surface" grids. At each grid point, we model only one dipole, oriented normally to the cortical surface.
2.Loose contraints---Only for "surface" grids, at each point in the surface grid the dipole direction is constrained to be normal to the local cortical surface.
3.Uncontrained---Either "surface" or "volume" grids. At each grid point, we leave undefined the assumed orientation of the source, such that three "elemental" dipoles are needed to model the source.

## Slide 3
Brainstorm源分析
1. 文件路径设置
..> config
..>> elec_file.xyz %电极坐标文件
..> Epoch_data %输入文件路径
..>> sub1.set %输入文件
..>> sub2.set %输入文件
..> Source_data %输出文件路径
..>> @default_study
..>> @default_subject
..>> @inter
..>> sub1 % sub1.set的输出路径
..>>> @default_study
..>>> @intra
..>>> ERP_data %运算结果的输出路径
..>>> **.mat %源分析结果文件
..>> sub2 % sub1.set的输出路径
..>>> @default_study
..>>> @intra
..>>> ERP_data %运算结果的输出路径
..>>> **.mat %源分析结果文件
2. 输入文件格式
setname-----ERP_data
filename-----sub*.set
EEG.event

## Slide 4
Brainstorm源分析
3. 创建protocol
File>>New protocol
处理协议名字
大脑结构像选择
大脑结构像路径：
源分析输出路径
源分析数据路径：
源分析输出路径
电极位置文件选择
4. 路径设置
clear;
close all;
PATHelec =‘***';
%电极文件的路径
PATHIN=‘***’;
%输入Epoch的路径
PATHOUT=‘***’;
%源分析输出路径
ProtocolInfo = bst_get(‘ProtocolInfo’);
%获取当前协议的信息
Path_bs=[ProtocolInfo.STUDIES filesep];
%获取当前协议的路径
elec_file=fullfile(PATHelec,‘elec_file.xyz’)
%读取电极文件
sFiles = [];%用于存放处理结果

## Slide 5
Brainstorm源分析
5. 导入Epoch文件
cd(PATHIN)
list=dir(‘*set’);
%获取PATHIN下Epoch文件的列表
len=length(list);
sFiles=bst_process('CallProcess',…
'process_import_data_epoch', ...
sFiles, [],'subjectname',subj{s}, ...
'condition', ‘ ', ...
'datafile',{{[PATHIN list(s).name ]},…
'EEG-EEGLAB'}, ...
'iepochs',[], ...
'eventtypes', 'type', ...
'createcond', 1, ...
'channelalign',0, ...
'usectfcomp', 0, ...
'usessp', 0, ...
'freq', [], ...
'baseline', []);
6. 设置电极文件
sFiles = bst_process('CallProcess',
'process_import_channel',sFiles, [], ...
'channelfile', {elec_file, 'EEGLAB'}, ...
'usedefault', 1, ...
'channelalign', 0);
sFiles = bst_process('CallProcess',
'process_noisecov', sFiles, [], ...
'baseline', [-0.35, 0], ...
'datatimewindow', [], ...
'sensortypes','', ...
'target', 1,'dcoffset',1, ...
'identity',0,'copycond',0, ...
'copysubj',0,'replacefile',1);
7.计算噪声(或数据)的协方差
sFiles = bst_process('CallProcess',
'process_average', sFiles, [], ...
'avgtype',1, 'avg_func',1, ...
'weighted',0, 'keepevents', 0);
8. 求取ERP

## Slide 6
Brainstorm源分析
9. 计算前向模型
sFiles = bst_process('CallProcess',
'process_headmodel', sFiles, [], ...
'Comment', '', ...
'sourcespace', 1, ... % Cortex surface
'volumegrid', [], ...
'meg',2, ... % Single sphere
'eeg',3, ... % OpenMEEG BEM
'ecog',2, ... % OpenMEEG BEM
'seeg', 2, ... % OpenMEEG BEM
'openmeeg', struct(...
'BemFiles', {{}}, ...
'BemNames',{{'Scalp', 'Skull', 'Brain'}}, ...
'BemCond', [1, 0.0125, 1], ...
'BemSelect', [1, 1, 1], ...
'isAdjoint', 0, ...
'isAdaptative',1, 'isSplit',0, ...
'SplitLength', 4000));
sHeadModel =bst_get('HeadModelForStudy',
sFiles(1).iStudy);
10. 溯源分析
sFiles = bst_process('CallProcess',
'process_inverse_2016',sFiles,[],...
'output', 2,
'inverse', struct(...
'Comment','dSPM: EEG', ...
'InverseMethod','minnorm', ...
'InverseMeasure','dspm', ...
'SourceOrient', {{'fixed'}}, ...
'Loose',0.2, ...
'UseDepth',1, ...
'WeightExp',0.5, ...
'WeightLimit', 10, ...
'NoiseMethod','reg', ...
'NoiseReg',0.1, ...
'SnrMethod','fixed', ...
'SnrRms',1e-06, ...
'SnrFixed',3, ...
'ComputeKernel', 1, ...
'DataTypes', {{'EEG'}}));

## Slide 7
Brainstorm源分析
11. 提取深部脑区的时间序列
% 这里选用Destrieux脑分区表示大
% 脑的ROI
sFiles = bst_process('CallProcess',
'process_extract_scout', ...
source_file, [], ...
'timewindow',[], ...
‘scouts’,{‘Destrieux’, …
{'G_Ins_lg_and_S_cent_ins R'}}, ...
'scoutfunc', 1,'isflip', 1, ...
'isnorm',0, ...
'concatenate',1,'save',1,...
'addrowcomment', 1, ...
'addfilecomment', 1);
Brodmann
Area
Destrieux

## Slide 8
Brainstorm链接分析
Non-directed
Correlation
Bivariate Granger causality
Time-resolved correlation
Directed
Coherence
Phase locking value
Amplitude envelope correlation
Bivariate Granger causality(spectral)
Phase transfer entropy
Time-resolved coherence
Time domain
Frequency domain

## Slide 9
Brainstorm链接分析
FC1. Pearson correlation
corr(F3,P3)反映了F3电极EEG和P3电极EEG的线性相关系数
% Process: Time-resolved correlation NxN
sFiles = bst_process('CallProcess',
'process_corr1n_time', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG', ...
‘includebad’, 1,‘win’,0.1, ... %窗宽100ms
‘overlap’, 50, ... %步长50ms
'scalarprod', 0, ...
'commenttag', '');
%% Process: Correlation NxN
sFiles = bst_process('CallProcess',
'process_corr1n', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG', ...
'includebad', 1, 'scalarprod', 0, ...
'outputmode', 1,'save', 1, ...
'addrowcomment', 1, ...
'addfilecomment', 1);
动态相关
静态相关

## Slide 10
Brainstorm链接分析
FC2. coherence
相干
coherence(F3,P3,f)从频谱的角度反映了F3电极EEG和P3电极EEG在f频率段的同步特性
f1
f2
fn
%% Process: Coherence NxN
sFiles = bst_process('CallProcess',
'process_cohere1n', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG', ...
'includebad',1, 'removeevoked', 0, ...
'cohmeasure', 1, 'maxfreqres', 2, ...
'maxfreq', 60, 'outputmode', 1,...
'save', 1, 'addrowcomment', 1, ...
'addfilecomment',1);
动态相干
静态相干
% Process: Time-resolved coherence NxN
sFiles = bst_process('CallProcess', 'process_cohere1n_time', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG',
'includebad', 1, ...
'removeevoked', 0, 'win', 0.3,
'overlap', 50, 'cohmeasure', 1, ...
'maxfreqres', 12, 'maxfreq', 60, ...
'commenttag', '');
表示时间段T和频率段F里的相干性

## Slide 11
Brainstorm链接分析
FC3. Phase Locking Value
静态PLV
是序列x在频率λ处的相角
是序列y在频率λ处的相角
n为Epoch的数量
% Process: Phase locking value NxN
sFiles = bst_process('CallProcess',
'process_plv1n', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG', ...
'includebad', 1, ...
'freqbands', {'delta', '2, 4', 'mean';
'theta', '5, 7', 'mean';
'alpha', '8, 12', 'mean';
'beta', '15, 29', 'mean';
'gamma1', '30, 59', 'mean'}, ...
'mirror', 0, 'keeptime', 0, ...
'plvmeasure', 2, 'outputmode', 1);
PLV(F3,P3,f)从相位的角度更加严格地反映了F3电极EEG和P3电极EEG在λ频率段的同步特性

## Slide 12
Brainstorm链接分析
FC4. Bivariate Granger causality
静态GC
---(1)
---(2)
假设1---X对Y有单向影响: 式(1)X各项滞后项前的参数不为零。Y各滞后项前的参数整体为0 。
假设2---Y对X有单向影响:式(2)Y各项滞后项前的参数不为零。X各滞后项前的参数整体为0 。
假设3---Y与X有双向影响: 式(1)和(2)中X和Y各项滞后项前的参数不为零。
假设4---Y与X不存在影响: 式(1)和(2)中X和Y各项滞后项前的参数为零。
格兰杰检验是通过受约束的F检验完成：
例如: 检验假设2，包含X滞后项的回归的残差平方为RSSU，包含X滞后项的回归的残差平方为RSSR，
k为无约束回归模型的代估参数的个数。如果: F>Fa(m,n-k), 则拒绝原假设，则认为X是Y的格兰杰原因。
滞后期
%Process: Bivariate Granger causality NxN
sFiles = bst_process('CallProcess',
'process_granger1n', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG', ...
'includebad', 1,'removeevoked',0, ...
'grangerorder',10,'outputmode',1,...
'save',1,'addrowcomment', 1, ...
'addfilecomment', 1);
From
To
GC反映了在认知过程中不同脑区之间的相互影响以及影响强度。

## Slide 13
频域格兰杰计算流程
Time series data
Model coefficients and residuals
Cross-spectral
Density matrix
Noise covariance matrix spectral transfer function
Granger causality
Autoregressive
model estimation
Spectral estimation using Fourier
decomposition and multitapering
Fourier transformation
of model coefficients
Factorization of spectral
density matrix
Estimation of Granger causality
Parametric approach
Non-parametric approach

## Slide 14
Brainstorm链接分析
FC5. Bivariate Granger causality(Spectral)
% Process: Bivariate Granger
% causality (spectral) NxN
sFiles = bst_process('CallProcess',
'process_spgranger1n', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG', ...
'includebad', 1, 'removeevoked', 0, ...
'grangerorder', 10,'maxfreqres', 2, ...
'maxfreq', 100, 'outputmode', 1);
f1
f2
fn
AR-model’s residuals.
GC反映了在认知过程中不同脑区之间的相互影响以及影响强度。

## Slide 15
Brainstorm链接分析
FC6. Amplitude envelope correlation
N为Epoch的总数。
包络相关
Trial之间包络相关的平均值：

## Slide 16
Brainstorm链接分析
FC6. Amplitude envelope correlation
% Process:
%Amplitude Envelope Correlation(NxN)
sFiles = bst_process('CallProcess',
'process_aec1n', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG', ...
'includebad', 1, ...
'freqbands', {
'delta', '2, 4', 'mean';
'theta', '5, 8', 'mean';
'alpha', '9, 12', 'mean';
'beta', '15, 29', 'mean';
'gamma1', '30, 59', 'mean';
'gamma2', '60, 90', 'mean'}, ...
'isorth', 0,'outputmode', 1);
AEC从包络的角度反映了认知过程中不同脑区之间的耦合关系。

## Slide 17
Brainstorm链接分析
Neural mass model parameters
A. NMMs are based on a physiologically plausible model of interactions between neuron populations in two similar brain areas. The neural activity in Area 1 (Signal 1) drives the neural activity in Area 2 (Signal 2) with an interaction lag of δ ms and a coupling strength of C.
B. We used NMMs to produce 1.5 s time-series of Signal 1 and Signal 2. Signals are represented either in the absence of noise (SNR = 45 dB) or with added simulated noise (SNR = 0 dB). Unless stated otherwise, metrics were computed from the central 500 ms segment (shaded area) of each signal.
C. Power spectra for normalized Signal 1 and Signal 2 for different coupling values were similar regardless of coupling strength.
Differences in metric value for different coupling strength were not a consequence of differences in signal power.
Normalized signals' power averaged over 100 simulations for each coupling value is plotted as a function of frequency.

## Slide 18
Brainstorm链接分析
FC7. Phase transfer entropy
是原序列X(t)通过复杂滤波求得(比如小波变换,希尔伯特变换)
在一给定的频段里，序列X(t)的瞬时相位时间序列θ(t)。
θx(t’)和θy(t’)是时间点t’ =t-δ的状态。即为θx(t’)= θx(t’ =t-δ), θy(t’)= θy(t’ =t-δ)
信息熵和联合熵

## Slide 19
Brainstorm链接分析
FC7. Phase transfer entropy
% Process: Phase Transfer Entropy NxN
sFiles = bst_process('CallProcess',
'process_pte1n', sFiles, [], ...
'timewindow', [-0.35, 0.998], ...
'dest_sensors', 'MEG, EEG', ...
'includebad', 1, ...
'freqbands', {'delta', '2, 4', 'mean';
'theta', '5, 8', 'mean'; 'alpha', '9, 12', 'mean';
'beta', '15, 29', 'mean';
'gamma1', '30, 49', 'mean';
'gamma2', '60, 90', 'mean'}, ...
'mirror', 0,'normalized', 1, ...
'outputmode', 1);
Theta_PTE
Alpha_PTE
PTE测量了认知过程中不同脑区之间
信息流动的方向和强弱，反映了认知
过程中不同脑区之间的耦合关系。